FISE2 - INFO2- HPP
2019-2020
Introduction to SIMD – MMX/SSE/AVX
Guillaume MULLER

---
Why having HPP lectures in FISE2?
Why HPP ?
- Classical approach to HPP = distribute on cluster
  - What if the initial code is inefficient?
  - ⇒ optimize locally first!
- Current machines already are massively parallel
- A large part of optimizations can not be vreated automatically
  - ⇒ impossible to rely on tools written by others
  - ⇒ as (future) engineers in CS: mandatory knowledge

---
Why SIMD/MMX/SSE/AVX?
- Task Parallelism
  - Execute coarse-grained pieces of code on ≠ pieces of hardware
  - Multi-cores, hyper/multi-threading…
- Instruction/Data Parallelism
  - Tiny pieces of code/data simultaneously on = hardware

---
"ça dépend, ça dépasse"?
Users
- Developers
- Compilers
Past
- Needs
- Capacities
- Errors
Future
- Dream
- New needs
- New capacities
Designor
micro-architecture
Electronic
- Physical Limits
- Complexity
Who has already used/programmed a processor ≠ Intel?
[Speaker Notes: 4 directions connaître le passé et avoir en tête un but futur répondre aux besoins des utilisateurs/dev sans casser la tête aux micro-architectes/compilateurs ou refaire les erreurs du passé Coincé entre 4 besoins contradictoires => Plein de questions vont se poser au concepteur de l’architecture et la réponse la plus courante sera “ça dépend” ! Il existe pleins de possibilités pour chaque choix => Il existe plein de combinaisons => Il existe plein d’architecture de processeurs différentes Ex: #registers, registers size, ...]

---
“Rappels”
store
load data
decode
execute
load instr.
IP
registers
- IP/JMP
- LD/ST
- ADD/SUB/MULT/DIV/...
Instruction Cycle:
- Fetch
- Decode
- Execute